## Slide 1: Integrated task 11
Analise

## Slide 2: Principle A
Increasing the time of the collision or the time the occupants take to stop
example 'crumple zones', physics - Impulse -reduces force I.e impact of crash

## Slide 3: Principle B
Spreading the forces of impact over the largest possible area & ensuring stability of the vehicle.
example 'crumple zones' impact/force is spread
example 'cars lower to ground' - ensures stability - refers to lower centre of gravity.

## Slide 4: Principle C
Minimizing contact of the person with the interior of the vehicle
example 'air bags/seat belts' - stops transfer of energy

## Slide 5: Principle D
Keeping the person inside the vehicle
example 'seat belt' - law of inertia - stops person from flying out

## Slide 6: Mercedes Benz B-Class 2016
Safety features of a Mercedes Benz B-class
ABS
Stability control - Stability control automatically senses when the vehicles handling limits have been exceeded and reduces engine power and/or applies select brakes to help prevent the driver from losing control of the vehicle.
Overhead airbags
Front -impact airbags
Side-impact airbags
Knee airbags - Knee airbags help to protect the occupants' lower extremities from serious injury in the event of an accident.
Anti-whiplash
Security system
Pretensioners - Seatbelt pretensioners automatically tighten seatbelts to place the occupant in the optimal seating position during a collision.

## Slide 7: Classify each feature as either A, B, C or D according to the principle/s it is employing

## Slide 8: 1955 Chevrolet
People may think highly of these cars if you ask a classic car guy his Favorite 8 out of 10 will say this car
But as it turns out the car itself isn't very safe and can have a lot of damage done if it is in an accident
The dash of the car had no cushion on it so the only thing in the way of skull crushing metal was paint
The front bench seats of the car were bolted down by only a handful of bolts and has no seatbelts so if you were to get in a collision you would become a human pinball in the cockpit
The doors in the car were no better if they didn’t pop open in a crash, they would fold in on themself and jam the car shut also the window crank looks like it was designed to Gouge flesh so if would be like you were in animal trap if you crashed this car

## Slide 9: Classify each feature as either A, B, C, D according to the principle/s it is not employing, and which therefore makes it unsafe.

## Slide 10: The role of safety in a car design
Safety features in a car are to provide the best chance to survive a crash or to avoid one all together

## Slide 11: Improvements using principles of physics